## Slide 1: Edge Devices for Automatic In-Field Bee Counting
Daniel Petti, Changying Li, Rachel Mallinger
FLASABE 2026
Ft. Myers, Florida
1
1
2
Ag. And Bio. Engineering Department, University of Florida
Entomology And Nematology Department, University of Florida

## Slide 2: Introduction
Blueberry growers depend on honeybees for pollination.
  It can be difficult to determine effectiveness.
Current method requires manual counting
Computer vision can be very effective for object counting.
  However, SoTA systems typically require lots of compute.

## Slide 3: Objectives
Develop a custom low-cost camera system for automatic bee counting.
Demonstrate a novel active learning approach for bee detection.
Show that lightweight tracking methods are practical for bee counting.

## Slide 4: Methods
Camera Module
Our system uses a custom camera module.

## Slide 5
Main Camera
IR Camera
Raspberry Pi
PoE Hat
Hailo 8
26 TOPS
2.5W Power

## Slide 6: Hivemind System
Supplies power to cameras
Stores data produced by cameras
Solar Panel
Battery
Mini
PC
PoE Switch
Camera

## Slide 7: Bee Detection Dataset
One of us (Dr. Mallinger) had many videos of hive entrances.
  We manually annotated a fraction of these data.
We also collected data from blueberry bushes at Citra.
Combined with about 400 images from a public dataset
Dataset is mostly A. Millefera with a few Bombus examples.
Public
Citra
Hives

## Slide 8: Data Annotation
In total, 44 images were annotated using RoboFlow.
  Combined with 400 public images
Annotations included head and abdomen locations.
  Indicate bee direction, which is useful for tracking
We used a custom active learning method to select data to annotate.
Notes: Statistics for dataset

## Slide 9: Active Learning
Notes: Selects images to annotate from a corpus of unannotated data.
Preliminary detections from the model are saved.
  Then corrected by a human
Added to the dataset and used to re-train the model
Selections are performed based on detector confidence
  Looks for a good mix of high and low-confidence detections (evenness)
  Also looks for medium-confidence detections (sweet spot)

## Slide 10: Tracking
Tracking is implemented using the BotSORT tracker
Uses detections from the camera as input
This is very computationally inexpensive.
  Can easily run in realtime on the controller
However, we are developing a more sophisticated tracker for future use.
  Uses a custom, deep-learning-based approach
Notes: -

## Slide 11: Software Deployment
The detection model is compiled for the Hailo 8 accelerator.
  Runs in real-time directly on the camera.
This allows us to intelligently choose when to save data.
Trackers for all cameras run on the Hivemind controller.
  This might change if the tracker becomes more difficult to run.

## Slide 12: Active Learning Results
Performance improves with more data.
Started with YOLO26n and scaled up to YOLO26s
Note that the validation set is exclusively drawn from the hive data.
Public data added here

## Slide 13: Tracking Results
Tracking works well on public data.
Achieves HOTA of 0.47 and IDF of 0.54
Even handles cases where bees are interacting.

## Slide 14: Tracking Results
Performance is also passable on hive data.
This is a trickier scenario
  Bees are more dense
  Quality is worse
Could possibly benefit from a more sophisticated tracker.

## Slide 15: Tracking Results
Can also track bees in videos of flower clusters.
These are generally easier due to low bee density.

## Slide 16: Conclusion
Counting bees is crucial to understanding blueberry pollination.
We developed an automated system to do this in the field.
  The system is scalable and uses low-cost hardware.
We developed a custom computer vision system to detect and track bees.
Overall, our method is effective in a range of environments.

## Slide 17: Thank You!
daniel.petti@ufl.edu
LIFT AI Grant
Dr. Patricio Munoz
Dr. Paul Lyrene
uflbsail.net